## Slide 1: Networks Are Hard, Evaluation Shouldn’t Be! Building an Open Platform to Evaluate AI Agents Beyond the Operator’s Wall
Alessandro Cornacchia
Global Connect 2026 | 14-15th September
Notes: Thanks for the introduction, and many thanks for the kind hospitality here in Paris! Yeah so today I’d like to share our ongoing experience with agentic benchmarks for telco, why they are important, and how does it look like to build them from the perspective of a research community, without having YET access to operator’s infrastructure

## Slide 2: Network issues: ever-present and costly
degrade user experience
loss of revenue
significant human-time to recover
NetSeer [SIGCOMM’20]
Issue localization 90% of downtime @ Alibaba
Notes: No matter how hard we try, network issues are inevitable and cost significant economic value to network providers. Part of the revenue loss comes from the fact that end users are not able to access their services, but another hidden cost lies behind the human engineering effort that is needed to resolve them. For example,

## Slide 3: Automation with AI agents (NetOps)
LM
Language Model
”monitor queue occupancy in switch S1 “
Network metrics
RTT, RDMA counters, ..
NetFlow
INT
Sketches
Active probing
SNMP logs
Switch CLIs
Topology
Environment / Tools
Web access
Language Models (LMs) + ability to interact with external environment
Notes: Well, because language models can geenrate text, ..

## Slide 4: Automation with AI agents (NetOps)
LM
Language Model
”monitor queue occupancy in switch S1 “
"tool": ”enable_INT",
"inputs": {
"switch": "S1"
}
function call
generates instructions to dictate which tool to use
Network metrics
RTT, RDMA counters, ..
NetFlow
INT
Sketches
Active probing
SNMP logs
Switch CLIs
Topology
Environment / Tools
Web access
Language Models (LMs) + ability to interact with external environment
Notes: Well, because language models can geenrate text, ..

## Slide 5: Automation with AI agents (NetOps)
LM
Language Model
”monitor queue occupancy in switch S1 “
"tool": ”enable_INT",
"inputs": {
"switch": "S1"
}
function call
generates instructions to dictate which tool to use
Language Models (LMs) + ability to interact with external environment
tool executed
Network metrics
RTT, RDMA counters, ..
NetFlow
INT
Sketches
Active probing
SNMP logs
Switch CLIs
Topology
Environment / Tools
Web access
Notes: Well, because language models can geenrate text, ..

## Slide 6: Agents are (complex) systems
HARNESS
Context
prompts, memory
Tool routing
validate calls
Guardrails
sandbox, policy
Loop control
reasoning workflows, retries
LM
”monitor queue occupancy in switch S1 “
The harness, not the model alone, decides what the agent sees, what it may do and when it stops
Agent = model + harness
Environment
The defining feature of an agent is not tool use, it is the feedback loop!
Notes: Well, because language models can geenrate text, ..

## Slide 7: Pain points today
Operators want to rapidly iterate and validate agentic NetOps solutions: did the change actually improve the agent?
Wait for a similar incident to happen again? → Slow
Reproduce the incident? → Impact on customers
Reproducibility
Almost impossible: incidents usually result from a combination of system, configuration, traffic and device errors.
Fairness
Operator A claims X%
Operator B claims Y%
who has the best agent?
🤔
model
context
prompt
tool-calling policy
RAG / troubleshooting workflows
NetOps?
Notes: After a real incident postmortem, we may realize that an agent failed to query a critical telemetry signal or jumped to a conclusion too early. We may then update the prompt, change the tool-calling policy, redesign the troubleshooting workflow, add RAG, or introduce multi-agent collaboration. But the key question immediately becomes: Did this change actually improve the agent?
From our observation, teams have no alternative but to deploy new strategies to the production environment and wait for similar incidents to happen again. The feedback loop is slow, noisy, and difficult to control. Real incidents are hard to reproduce, production networks cannot be freely used for fault injection, and human labels may vary across incidents.

## Slide 8: We need a standardized, open benchmark
Oct 2023
SWE-bench
Software engineering
Resolve real GitHub issues
2,294 tasks, 12 repos
Unit-test verified
Jun 2024
τ-bench
Customer service
Agent ↔ user sim + tools
Retail & airline policies
pass^k reliability
Jul 2024
AppWorld
Everyday app automation
9 apps, 457 APIs
750 day-to-day tasks
State-based checks
Jan 2025
AIOpsLab
Cloud operations (AIOps)
Live microservice stacks
Inject, detect, mitigate faults
Microsoft · MLSys ’25
May 2025
Terminal-Bench
Terminal / sysadmin
Real CLI tasks in Docker
Compile, configure, debug
Stanford + Laude
Jul 2025
BFCL v4
Tool / function calling
Agentic web search, memory
Multi-turn, format sensitivity
Live leaderboard
Aug 2025
WideSearch
Broad information seeking
200 wide web-search tasks
Completeness-checked tables
ByteDance Seed
Apr 2026
Claw-Eval
General autonomous agents
300 human-verified tasks
Full-trajectory auditing
Completion, safety, robustness
Notes: These benchmarks are not only useful for reproducibility and fairness, but I would also argue they

## Slide 9: Telco benchmarks measure understanding, not operation
Evaluated against
offline verifier: syntax, schema, intent
✗ Network in closed-loop
offline control-plane validator
Evaluated against
annotated ground truth
✗ Network in closed-loop
offline logs and telemetry
Necessary, but not sufficient
Network Configuration
Troubleshooting / RCA
NetConfEval [2024]
Cornetto [2026]
TeleYAML [2025]
Real network operations
Evaluated against
reference answer, exact match
only evaluate model-knowledge and recall
Standard & Domain Knowledge
TeleQnA [2023]
3GPP-TSG [2025]
TeleMath [2025]
TeleTables [2025]
TeleLogs [2025]
AI Telco Troubleshooting Challenge [2025-26]
👷
👷
👷

## Slide 10
“OTel-2.0-LLM-31B-IT is a telecom-specialized instruction model post-trained from Gemma 4 31B-IT”

## Slide 11: Ideal requirements for a NetOps benchmark
variety
scale
realism
Cornetto
NetArena
Open Telco
AI (GSMA)
NetConfEval
NIKA
[2025]
NetOpsBench
[2026]
FauIT-Bench
[2026]
CTBench
[2026]
requires a joint
effort!
Notes: Represent as an intersection of circles and show that today I want to deal with realism. (defined later)
Concede to NetOpsBench and the Huawei one that interacts with real devices that cited NIKA, add years and make emerging areas

## Slide 12: NIKA
Network Incident Benchmark for AI Agents

## Slide 13: Challenges & Contributions
Realism
=
Network environment
+
Incident data
+
Closed-loop agent interaction
Lack of real data: proprietary incident reports and troubleshooting workflows
Network emulators
+
synthetic incident injection
APIs for developer that make building new scenarios fast and systematic
Agent-Network Interfaces
for agents to interact with network telemetry
telemetry
tools
configurations
protocols
Notes: Unlike SWE-bench, there is no public corpus of real network incidents to build on

## Slide 14: NIKA: synthetic incident injection
Notes: here you will add SNDlib topologies and table + traffic workloads

## Slide 15: NIKA: synthetic incident generation
[1] Orlowski, Sebastian, et al. "SNDlib 1.0—Survivable network design library." Networks: An International Journal 55.3 (2010): 276-286.
Abilene from SNDlib[1]
nodes • links • capacities • demand matrix
Notes: here you will add SNDlib topologies and table + traffic workloads

## Slide 16: From specs to a runnable NIKA scenario
Vendor docs
ISP/operator guides
RFCs
Community practice
2
1
Distill operator practices
Start from real topology
3
Derive intents as intermediate representation
4
Materialize runnable artifacts
AI turns into explicit plans & specs
e.g., Abilene from SNDlib[1]
nodes • links • capacities • demand matrix
Example design principles
Net configs
Backend recipes
IGP scoped within domain
RR-based iBGP
topology-derived metrics
explicit prefix policy
Abilene design
Network intent
12 routers mapped
/31 links + loopbacks
RR / client roles
prefixes placed at edges
prefix reachability (*,P)
waypointing (A,B)
load balancing
etc.
Benchmark curators implement on backends
Notes: TODO: here can introduce tension between Realism and Variety (in the last step)

## Slide 17: Network issues injection: taxonomy
Link down / flap · faulty cable · silent packet loss · capacity bottleneck
Link & vNICs
6
BGP ASN mismatch · RPKI-invalid route leak · OSPF area misconfig · router crash
Routing & Control Plane
8
ACL blocks · SDN flow-rule loops · P4 pipeline mismatch · MTU · WireGuard · K8s policy
Forwarding, Encap. & Policy
26
ClusterIP failure · load-balancer overload · SNAT port-pool exhaustion
Service Networking
6
K8s API-server partition · SDN controller crash · southbound port unreachable
Management & Orchestration
4
IP / MAC conflicts · wrong netmask · DHCP & DNS spoofing · DNS path block
Addressing, Neighbor & Naming
13
Sender CPU contention · receiver resource contention
Endpoint & Application
2
Incast traffic · late ECN marking · TCP receive-window limited
Traffic, Queueing & Resource
3
ARP cache poisoning · BGP hijacking · DHCP spoofing · SYN flood · service DoS
Security
7
# of supported synthetic failures
Growing set…
75
N

## Slide 18: How came?
Post-mortems in technical blogs
e.g., bgp_max_prefix_exceeded: Optus outage, APNIC (2023). NIKA advertises excess prefixes to an eBGP peer with a configured limit. The receiving router tears down the BGP sessions.
Peer-reviewed academic paper
e.g., slient_egress_packet_loss: Everflow [SIGCOMM’15]. NIKA reproduces a programmable forwarding fault where selected traffic is dropped while ordinary counters remain healthy.
RFC / Standards
e.g., mtu_mismatch: TCP Problems with Path MTU Discovery [RFC 2923]. NIKA lowers the MTU on an intermediate L3 hop. Small packets remain reachable, while oversized DF packets trigger ICMP “Fragmentation Needed”.
Vendor troubleshooting guides
e.g., nat_mapping_removed_without_drain: Google Cloud NAT troubleshooting guidance. NIKA removes NAT/address state before existing flows drain, reproducing disruption caused by unsafe NAT lifecycle changes.

## Slide 19: NIKA Orchestrator
Notes: TODO: change title

## Slide 20: NIKA Orchestrator
|N| x |T| x |I|
programmatic
mutations
Notes: here you will add SNDlib topologies and table + traffic workloads

## Slide 21: NIKA
Notes: here you will add SNDlib topologies and table + traffic workloads

## Slide 22: Before testing the agent, test the benchmark!
Net configs
Backend recipes
curator
Notes: TODO Might need some intro to recall the configurations can have bugs and are human made

## Slide 23: Before testing the agent, test the benchmark!
healthy network
initial environment
symptoms caused by the injected fault
benchmark task
fault injected
no failure symptoms
Net configs
Backend recipes
curator
Notes: TODO Might need some intro to recall the configurations can have bugs and are human made

## Slide 24: Before testing the agent, test the benchmark!
Net configs
Backend recipes
Notes: TODO Might need some intro to recall the configurations can have bugs and are human made

## Slide 25: Before testing the agent, test the benchmark!
silent failures
initial (mis-)configuration
no symptoms
Net configs
Backend recipes
unexpected symptoms
Notes: TODO Might need some intro to recall the configurations can have bugs and are human made

## Slide 26: Before testing the agent, test the benchmark!
silent failures
initial (mis-)configuration
no symptoms
Net configs
Backend recipes
unexpected symptoms
silent failures contaminate tasks
may dominate the ground-truth
caused by the injected fault
Notes: TODO Might need some intro to recall the configurations can have bugs and are human made

## Slide 27: Before testing the agent, test the benchmark!
1. Validate the healthy scenario (Walkthrough example: isp_abilene scenario)
A
Control-plane analysis
Does the intended forwarding behavior
follow from the configuration?
B
Runtime verification
Did the emulated network start and converge?
C
Behavioral validation
Does the live network satisfy the design intent end to end?
Inject fault: advertise excess prefixes to the receiver
2. Validate after fault injection (Walkthrough example: bgp_max_prefix_exceeded failure)
D
Validate the fault artifact
Did NIKA reproduce the intended failure?
E
Validate the observable symptom
Does the fault produce the expected observable symptom?
e.g., the target eBGP session is allowed and expected routes are present.
e.g., all expected links and routing sessions are up, and the target eBGP session is established.
e.g., customer-side reachability is normal before fault injection.
e.g., the edge router reaches the protective limit and tears down the peer session.
e.g., traffic through the affected peer loses reachability after the reset.
E2E Tests
E2E Tests
Integration Tests
Integration Tests
F
C
Behavioral validation
(Repeat)
Notes: TODO: if there is time add: - “audit based on thresholds”
- tension with variety

## Slide 28: NIKA
Evaluation

## Slide 29: Agents can find the fault, but rarely explain it
Performance of GPT-based agent for detection, localization and root cause analysis
HF: Host Failure, LF: Link Failure, MC: MisConfiguration,
NA: Network under Attack, NE: Network node Error, RC: Resource Contention.
Dec’ 25

## Slide 30: Agents can find the fault, but rarely explain it
K. H. Tseng et al. SADE: Symptom-Aware Diagnostic Escalation for LLM-Based Network Troubleshooting [IEEE LCN’26]
May’26
Dec’ 25

## Slide 31: Agents can find the fault, but rarely explain it
K. H. Tseng et al. SADE: Symptom-Aware Diagnostic Escalation for LLM-Based Network Troubleshooting [IEEE LCN’26]
May’26
Dec’ 25
Harness
Troubleshooting
skills
Better scaffolding partially closes the gap

## Slide 32
May’26
Dec’ 25
Sep’26
https://sands-lab.github.io/nika/leaderboard
🔜👀
next chapter with AI4NET Lab

## Slide 33: Main insights
Agents make structured tool use, however only a stronger backbone model drive behavior towards broader tool use and connecting outputs with deeper root causes

## Slide 34: Main insights
Agents make structured tool use, however only a stronger backbone model drive behavior towards broader tool use and connecting outputs with deeper root causes

## Slide 35: Main insights
Agents make structured tool use, however only a stronger backbone model drive behavior towards broader tool use and connecting outputs with deeper root causes
Network troubleshooting stresses agents to deal with partial observability, multi-step reasoning, structured tool use
  Silent errors may not leave an explicit error message
  Faults may compound, requiring multiple diagnose actions

## Slide 36: Main insights
Agents make structured tool use, however only a stronger backbone model drive behavior towards broader tool use and connecting outputs with deeper root causes
Network troubleshooting stresses agents to deal with partial observability, multi-step reasoning, structured tool use
  Silent errors may not leave an explicit error message
  Faults may compound, requiring multiple diagnose actions
Agents tend to stop at shallow, connectivity-centric explanations
  Vague diagnoses such as “connection unstable” or “transient congestion”, without connecting these symptoms to the deeper causes

## Slide 37
Agent fails to recognize this is a non-problem:
investigates and patches k8s coredns
creates new index in MongoDB database
Scenario: a microservice starts before its database is ready
A. Cornacchia, I. Alabdulaal, I. Saghier, A. Mirdad, O.Fayoumi, M.Canini. Between Promise and Pain: The Reality of Automating Failure Analysis
in Microservices with Large Language Models. [in ACM APSys’25]

## Slide 38
Agent fails to recognize this is a non-problem:
investigates and patches k8s coredns
creates new index in MongoDB database
faulty
healthy
Rabbit holes 
Scenario: a microservice starts before its database is ready
A. Cornacchia, I. Alabdulaal, I. Saghier, A. Mirdad, O.Fayoumi, M.Canini. Between Promise and Pain: The Reality of Automating Failure Analysis
in Microservices with Large Language Models. [in ACM APSys’25]

## Slide 40
Why agents fail?
And what should we do about that?

## Slide 41: Agentic workflow as state-space systems
A workflow can be viewed as a controlled stochastic search process over an evolving state space
Prompt
Dynamic
Stochastic
Dynamic
Stochastic
Behavior: Complex interactions between dynamic-stochastic program steps
“Feedback loop” unrolled view

## Slide 42: Unfulfilling recipe (today)
Improving agent performance is about eliciting the right behaviors
In optimization terms, for an agent A, we have:
We seek the better prompts, model parameters, tools to maximize the expected ability for A to reach the task’s goal
How? The usual AI soup: SFT, RLVR, GRPO, etc.

## Slide 43: Why unfulfilling?
We show the agent through many (~thousands) demonstrations how to correctly make use of tools and solve the tasks
There is no real magic … even for networked systems
  But cleverness matters.. agents need practice with real (complex) network problems!
An agent that does not “experience” dealing with network incidents is bound to do poorly
  Local single-cause diagnosis works for the overwhelming majority of incidents  A commit early and confidently to a local root cause
Notes: Suppose most examples contain one fault, close to the symptom, and the first plausible explanation is usually correct. An agent could perform well by learning to identify a familiar pattern and commit quickly.
This is what has been done until today, where dynamic benchmarks and environments were not here.
Now give it an incident where the symptom appears far from the cause, two faults interact, or the apparent failure is simply a service that has not finished starting. The same strategy can lead it in the wrong direction.

## Slide 44: A way forward: agents need to “experience” networked systems rigorously
Learning works, but what is learned and acted on matters
  Agents don’t fail because they lack reasoning power
  They fail because the required competence is a search policy that is absent from their training distribution
Rigorous analysis tools will help bridge the gap
(a short walk down on the memory lane)
“Here are the relevant observations. What explains them?”
“Here is a symptom. Find the observations needed to explain it.”
vs
Notes: And so where do we go from here? Well, I want to argue that a better way forward is for agents to experience networks and distributed systems in a more rigorous way.
Our experience with Nika has taught us that if you present the agent with the right evidence, with the right observation, it will likely give you a very convincing explanation, probably much more detailed of what any network engineer would be able to produce.
However this does not translate directly into reliable network investigation capabilities.
SO ..in other words.. my point is that.. today agents do not fail because they lack reasoning power. What they lack today is instead what I call the search policy, which is something that is absent from their training distribution, but would translate the strong reasoning capabilities of agents into reliable network investigation.
We instead need to teach the model through interactions with the system, supported by tools that make consequences of each action observable and testable.
And the networking community has useful experience to draw on here.

## Slide 45: Software Bugs in Inter-Domain Routers
Router type A
Router type B
At 17:07:26 UTC on August 19, 2009 CNCI (AS9354), a small network service provider in Nagoya, Japan, advertised a handful of BGP updates containing an empty AS4_PATH attribute. [renesys blog]
?
Reset session!
0-length AS4_PATH attribute!
Protocol-compliant, confusing message
A blast from the past

## Slide 46: What went wrong (session reset flood)
Unaffected router
Affected router
?
?
?
?
?
Unreachable!
Repeated service disruptions
A blast from the past

## Slide 47: Guard Against Possible Faults: Detect and Remove Them!
B
A
C
D
Time
Live
Testing (in parallel)
Account for current state, code and configuration
A blast from the past
Notes: The natural question was: could we detect this kind of problem before it disrupted the live network?
The idea shown here is to run testing alongside production. Take the current system state, code and configuration, and explore what could happen in an isolated environment while the live system continues operating.
Notice the emphasis on current state. We are not just testing some generic router in a generic network. We want the test to reflect the system we actually have.

## Slide 48: DiCE
BGP neighbors
BGP process
DiCE
Key idea: automatically explore system behavior to detect potential faults
  Create an isolated snapshot of a BGP neighborhood
  Subject a router’s BGP process to many inputs that exercise router actions
  For each input, check if the snapshot misbehaves
[USENIX ATC ’11]
A blast from the past
Notes: DiCE, presented at USENIX ATC in 2011, gives a concrete example of this approach.
First, create an isolated snapshot of a BGP neighbourhood. Then subject the router's BGP process to inputs that exercise different actions. For each input, check whether the snapshot misbehaves.
The central idea is systematic exploration. Instead of waiting for the right failure to arrive, we actively look for behaviours that violate our expectations.
That gives us a useful principle for agents today: create a place where they can investigate possible failures and test hypotheses, where the test environment supplies concrete evidence about what actually happens.

## Slide 49: BGP snapshot
Isolate testing from production environment
Local checkpoint of current state and configuration
BGP’s federated environment  Each router keeps its local checkpoint  Private state & config stays in the AS
A blast from the past

## Slide 50: Takeaway: Focus on tooling & interfacing
Agents need to “experience” networked systems rigorously
Rigorous analysis tools will help bridge the gap
  Network softwarization over the past decade laid a new foundation for rigorous, systematic interaction with networked systems
Let agents exploit rich tools and interfaces, guiding the search
  An agent is a reasonable glue layer around the right substrate — stand up the twin, invoke control-plane verification (Batfish / Minesweeper-style), run fault injection and what-if exploration, interpret results

## Slide 51
NETWORKS ARE HARD, EVALUATION SHOULDN’T BE!
Agents don’t fail for lack of reasoning. They lack an effective search policy.
This community should build it in!
sands-lab/nika
Code
Website
sands-lab.github.io/nika

## Slide 52
25
Backup: GPT-6 scores*
Codex + GPT-6 Astra
ReAct + GPT-6 Astra
Score (%)
0
20
40
60
80
100
96.4%
72.4%
Detection
79.8%
49.4%
Localization
F1 score
76.2%
49.4%
RCA
F1 score
*results computed on 3 runs of a 30-task fold of NIKA v2.0
Notes: Can build something more on top of “no fault injected” -> like enlarge the space and make clear it’s a large exploration space. Eventually the stable version of our benchmark emerged by several back and forth iterations where the troubleshooting agent and a judge worked together.

## Slide 53: Backup: Benchmarking under an evolving world
Today:
one snapshot
One task
Agent
Final configuration
Correct?
Assessed once, at one endpoint
Real operations:
requirements
accumulate
Introduce a
new service
Configuration 1
Change
routing policy
Configuration 2
Strengthen security boundary
Configuration 3
Change the infrastructure
Configuration 4
Time
Meets the new requirement, but overwrites behavior established earlier: a regression the snapshot never sees
Each change must respect prior requirements without introducing regressions.
Correct at one point in time is not the same as reliable as the network evolves.
Notes: need to highlight this doesn’t capture regressions. Might also need some introduction about currently we exclude mitigation.

## Slide 54: Backup: The CPU bottleneck and Sandboxing

## Slide 55: Do we blame the benchmark or the agent?
audit the benchmark first!
84
Submitted a label that is also true
of the injected state
77
Correct label submitted, together
with extra labels
41
Ground truth ≠ injected mechanism;
harness lost or never got the answer
40
Root cause exactly right,
device set mismatch
31
Fault leaves no symptom the
scenario's tools can see
25
Report names the mechanism,
submits a different label
906 runs
Decided by the benchmark 298 (33%)
Decided by the agent 608 (67%)
Notes: You might be tempted to stop at the accuracy numbers ,BUT
need to add some story-telling about networking-specific issues that may arise not intially accounted for. e.g., a failure injection method inadvertendly produce a second failure; the agent gets it right but the benchmark not!